## Slide 1
SRTA3353 MACHINE LEARNING FOR IOT | PROJECT 2
Machine Learning-Based Smart Irrigation System
Predicting soil dryness before plant stress occurs using Raspberry Pi 400, sensors, Streamlit, and notifications
Raspberry Pi 400
DHT11
Soil + MCP3008
Relay Pump
Streamlit
Telegram/Favoriot
PROBLEM & OBJECTIVE
From reactive watering to predictive irrigation
Traditional automatic watering only reacts when soil is already dry. The proposed system predicts whether soil will become dry soon using current environment and moisture trend.
Main ML output: Dry Soon / Not Dry Soon
Soil status threshold
DRY < 30%
OPTIMAL
WET > 70%
DECISION LOGIC
Safe hybrid control keeps the demo reliable
Condition
Recommend
Control
DRY
Pump ON
Pump ON
WET
Pump OFF
Pump OFF
OPTIMAL + Dry Soon
Alert only
Pump ON early
Demo setting: ML_CONTROL_MODE=recommend
SYSTEM ARCHITECTURE
Sensing, processing, action, and visualization are integrated in one loop
Sensors
DHT11 temp/humidity
soil sensor AO
ADC
MCP3008 converts analog soil signal to digital
Raspberry Pi
full_monitor.py
preprocess + predict
Outputs
relay pump, OLED,
Telegram alerts
Dashboard
plant_data.csv
Streamlit + Favoriot
Streamlit reads plant_data.csv while full_monitor.py writes new readings. Auto-refresh updates the dashboard display only.
HARDWARE IMPLEMENTATION
Required sensors and actuator are covered
Raspberry Pi 400 runs the monitoring script.
DHT11 provides temperature and humidity.
Soil moisture AO is read through MCP3008 channel 0.
Relay on GPIO18 controls the DC water pump.
OLED SSD1306 shows live local status.
Wiring hints: enable SPI for MCP3008, I2C for OLED, verify DHT pin D4/D17.
DATA PROCESSING & ML
The model predicts dryness in the next 10 minutes
Input
Processing
Output
Soil raw
calibrate
soil_value
Soil %
threshold
soil_status
Current/previous
subtract
change_rate
DHT missing
no average
Unknown
ML features: soil_value, temperature, humidity, previous_soil_value, moisture_change_rate, pump_status.
DASHBOARD & NOTIFICATIONS
Student 5 work: monitoring, alerts, and cloud path
Streamlit dashboard is the main monitoring interface.
Separate charts: soil moisture, temperature, humidity, moisture trend.
Alert banners for DRY, WET, Dry Soon, DHT Missing, and stale data.
Telegram sends alerts once per warning type per cooldown period.
Favoriot REST payload remains optional cloud visualization.
DEMO SCENARIOS
Show normal, abnormal, and ML-predicted states
Scenario
Action
Expected result
Optimal
medium-moist soil
Pump OFF
Dry
dry condition
Pump ON
Dry Soon
warm/drying trend
Alert
Wet
very wet soil
Pump OFF
DHT fault
missing DHT data
Unknown
ASSESSMENT EVIDENCE
The poster, demo, and report can point to each scoring area
Criteria
Evidence
Marks focus
Problem relevance
Predictive smart agriculture watering
5
Hardware integration
Pi 400, DHT11, soil, MCP3008, OLED, relay, pump
10
Data communication
Streamlit, CSV, Telegram, Favoriot REST payload
5
Decision logic
Threshold baseline + Decision Tree ML
5
Demo/documentation
README, Student Guide, tests, demo scenarios
10
Student 4
Data processing, missing-data handling, feature extraction, baseline vs ML comparison.
Student 5
Streamlit dashboard, charts, Telegram alerts, monitoring/debug, Favoriot connectivity.
Project files: full_monitor.py, streamlit_app.py, plant_monitor/, plant_data.csv, models/dryness_model.joblib
ML-Based Smart Irrigation System