## Slide 1
SRTA3353 MACHINE LEARNING FOR IOT
Machine Learning-Based Smart Irrigation System
Predicting soil dryness before plant stress occurs
Raspberry Pi 400 + DHT11 + soil sensor/MCP3008 + relay pump + OLED + Streamlit + Telegram/Favoriot
3
input sensor values
soil moisture, temperature, humidity
10 min
prediction target
demo can use 10 seconds
Hybrid
decision logic
threshold baseline plus ML
Live
monitoring layer
OLED, Streamlit, Telegram, Favoriot
Prepared for Project 2: Hardware-Based IoT System Implementation
01

## Slide 2
PROBLEM FIT
The system shifts irrigation from reactive watering to predictive warning.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
02
Traditional small-plant watering reacts only after soil is already dry. In hot or low-humidity conditions, that delay can stress the plant before the pump starts.
Baseline system
Soil is dry now -> pump ON. Simple and reliable, but late.
Project system
Soil is still optimal, but trend and environment show Dry Soon.
Outcome
Warn early, log evidence, and optionally control pump before stress.
Target users
Small plant owners, student labs, and greenhouse-style demos that need low-cost monitoring.
Application domain
Smart agriculture: soil moisture, temperature, humidity, irrigation automation, crop monitoring.

## Slide 3
CRITERIA COVERAGE
The prototype maps directly to the technical requirements.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
03
Assignment requirement
Implementation evidence
Raspberry Pi / hardware platform
Raspberry Pi 400 runs full_monitor.py
At least three input sensors/values
DHT11 temperature, DHT11 humidity, soil moisture via MCP3008
Output / actuator
Relay controls DC water pump; OLED shows local status
Real-time / near real-time processing
READ_INTERVAL_SECONDS=600 normally; 10 seconds for demo
Two data handling steps
Calibration to percent, thresholding, feature extraction, missing-data handling
Decision mechanism
Hybrid: baseline threshold plus DecisionTreeClassifier prediction
Monitoring layer
Streamlit dashboard plus OLED display
Automatic alert/control
Pump control, Streamlit banners, Telegram notifications
IoT visualization
Streamlit as main dashboard; Favoriot REST payload kept for cloud visualization
For final submission, include screenshots of Streamlit and Favoriot if the Favoriot device is configured.

## Slide 4
HARDWARE PROOF
The hardware path covers sensing, conversion, display, and actuation.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
04
DHT11
Temperature and humidity
Default pin: board.D4
Soil sensor AO
Analog moisture signal
MCP3008 ADC
SPI analog-to-digital
Soil channel: CH0
Raspberry Pi 400
Reads sensors, preprocesses, predicts, logs CSV, controls relay
OLED SSD1306
I2C display shows temp, humidity, soil, ML, pump
Relay + pump
GPIO18 active LOW
LOW = pump ON
Important wiring checks: enable I2C for OLED, enable SPI for MCP3008, verify DHT pin, verify relay active-LOW behavior.

## Slide 5
SOFTWARE FLOW
One Python loop connects hardware, ML, logging, and dashboards.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
05
Sensors
DHT11 + soil AO
full_monitor.py
read, preprocess, predict
Decision
threshold + ML
Outputs
pump, OLED, alerts
Data layer
CSV + dashboard + cloud
Telegram
risk alerts with cooldown
Streamlit
latest metrics, charts, debug status
Favoriot
optional REST cloud payload
Streamlit reads plant_data.csv. It does not directly read sensors or control the pump.

## Slide 6
DATA PROCESSING
Preprocessing turns raw sensor values into reliable ML features.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
06
Soil moisture status thresholds
DRY < 30%
OPTIMAL 30-70%
WET > 70%
0%
30%
70%
100%
Raw / issue
Processing method
Output
Soil analog reading
Calibrate to 0-100 percent
soil_value
Soil percentage
Threshold classification
DRY / OPTIMAL / WET
Current + previous soil
Feature extraction
moisture_change_rate
Pump ON/OFF text
Encode for ML feature
pump_status_code
Incomplete training row
Drop before training
clean dataset
Missing DHT11 data
Do not average; return Unknown
DHT Missing alert
Why missing DHT11 is not averaged
In real hardware, missing temperature or humidity may indicate wiring or sensor failure. Filling with an average can hide the fault and create fake weather conditions, so the safer output is ml_prediction = Unknown.
This covers the assignment requirement for at least two data handling or preprocessing steps.

## Slide 7
INTELLIGENCE
The ML layer predicts future dryness instead of replacing the safe baseline.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
07
Item
Baseline logic
ML intelligent logic
Main input
Current soil only
Soil, temp, humidity, previous soil, trend, pump
Decision
soil < 30% -> pump ON
Predict Dry Soon / Not Dry Soon
Behavior
Reactive
Predictive
Example
45% soil means pump OFF
45% + hot/dry/falling trend can mean Dry Soon
Default: recommend mode
ML warns early, but threshold keeps direct pump control safer for demos.
Optional: control mode
OPTIMAL + ML Dry Soon can turn pump ON early.
Model
DecisionTreeClassifier saved as models/dryness_model.joblib.

## Slide 8
MODEL DATA
Kaggle starts the model; real Raspberry Pi data improves it later.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
08
1. Starter training
Use data/training_smart_agriculture.csv.
MOI -> soil_value; temp/humidity retained.
2. Saved model
Train Decision Tree and save models/dryness_model.joblib.
3. Real-time prediction
full_monitor.py loads model and predicts every sensor cycle.
4. Retrain later
Use collected plant_data.csv after enough real rows.
Current behavior
The model loads or trains at startup. It does not automatically retrain every 10 minutes.
Retraining explanation for lecturer
If 20 days of real data exists in plant_data.csv, retraining uses the whole 20-day file unless manually filtered.

## Slide 9
DASHBOARD
Streamlit is the main live dashboard; Favoriot remains the IoT cloud path.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
09
Streamlit dashboard mock
45%
soil moisture
latest CSV reading
32 C
temperature
DHT11
55%
humidity
DHT11
OFF
pump
safe state
45%
soil
32 C
temp
55%
humidity
rate
trend
Charts are separated by unit: soil %, temperature C, humidity %, and moisture change rate.
Telegram
Sends risk alerts to personal or group chat with cooldown.
Favoriot
REST payload includes temp, humidity, soil, pump, ML, notification status.
OLED
Shows SMART PLANT, DHT status, soil value, ML prediction, and pump status.

## Slide 10
AUTOMATION
Pump control stays safe while alerts explain every risk state.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
10
Condition
Recommend mode output
Control mode output
DRY soil
Pump ON
Pump ON
WET soil
Pump OFF + wet alert
Pump OFF + wet alert
OPTIMAL + Dry Soon
Pump OFF + early warning
Pump ON early
DHT missing
ML Unknown + DHT alert
ML Unknown + DHT alert
Telegram cooldown
Same warning type sends once every 30 minutes normally, or every 60 seconds in demo mode.
Reason codes
PUMP_ON_DRY, PUMP_ON_ML_DRY_SOON, TELEGRAM_SENT, CSV_WRITE_OK, MODEL_LOADED.

## Slide 11
DEMO PLAN
A strong demo proves normal operation, abnormal states, and recovery.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
11
Demo scenario
Action to show
Expected evidence
Normal / optimal soil
Sensor in medium-moist soil
Pump OFF, dashboard updates
Dry soil
Expose sensor to dry condition
Pump ON, DRY alert
Dry Soon
Use warm/low humidity sample or model output
Early warning, pump OFF in recommend mode
Wet / overwatering
Place sensor in very wet soil
Pump OFF, WET alert
Hardware fault
Disconnect DHT11 briefly
ML Unknown + DHT Missing alert
Lecturer demo interval
READ_INTERVAL_SECONDS=10, NOTIFICATION_COOLDOWN_SECONDS=60, STREAMLIT_REFRESH_SECONDS=10.
Normal collection
READ_INTERVAL_SECONDS=600, NOTIFICATION_COOLDOWN_SECONDS=1800.

## Slide 12
SUBMISSION EVIDENCE
The final story should show working hardware plus clear individual contribution.
Source: project README, Student Guide, and SRTA3353 Project 2 criteria
12
Marking area
Evidence in project
Problem relevance (5)
Predictive smart agriculture watering before plant stress
Hardware integration (10)
Pi 400, DHT11, soil sensor, MCP3008, OLED, relay, pump
Data communication (5)
Streamlit, CSV logging, Telegram, Favoriot REST support
Decision logic (5)
Threshold baseline plus Decision Tree ML prediction
Presentation/documentation (10)
README, Student Guide, tests, demo scenarios, contribution evidence
Student 4 evidence
Preprocessing, missing data handling, feature extraction, ML decision, baseline comparison.
Student 5 evidence
Streamlit dashboard, charts, Telegram alerts, cloud/Favoriot payload, monitoring/debug tab.